## Slide 1: Security – V1
R1
R2
R3
R4
SW2
SW1
SW3
SW4
R5
VLAN_3
VLAN_55
VLAN_155
VLAN_33
VLAN_2
VLAN_155
OSPF 0
EIGRP YY
F/R
F/R
DMZ3
Inside
Outside
S1/0.24m
24.0
S1/0.23m
23.0
F0/0
33.0
55.0
155.0
ASA
VLAN_5
E1.3
E1.2
E0
E3
F0/1
VLAN_25
F0/0
F0/1.2
F0/0
F0/1.1
25.0
5.0
2.0
F0/0
3.0

## Slide 2: Security – V1
YY.YY번호 = 43.43
Loopback0
  32비트
  43.43.0.x
  라우팅 프로토콜에서 광고하지 말 것
SW1 – 4
  Vtp Server/Client
  Vtp domain: ccie
  Vtp password: cisco
  필요 vlan 생성
    Vlan 100 포함
  Lo0 생성하지 말 것
SW1
  Int vlan 155
    43.43.155.250/24
SW2
  Int vlan 55
    43.43.55.250/24
SW3
  Int vlan 33
    43.43.33.250/24
SW4
  Int vlan 2
    43.43.2.250/24
  Static: Default 설정
    43.43.2.253

## Slide 3: Security – V1
R1
  Lo100
    111.111.111.111/24
  Static: Default 설정
R2
  Lo100
    222.222.222.222/32
  Static: Default 설정
    43.43.5.253으로
R5
  Lo100
    155.155.155.155/32
  EIGRP & OSPF 양방향 재분배
FR 구간 인터페이스
  OSPF Network Broadcast 설정
R2
  OSPF에서 Default 설정

## Slide 4: ASA
Default Route
  43.43.5.2(F0/0 on R2)
ASA1/AS2
  Multi-context router mode
    Admin: admin.cfg
    R1: R1.cfg
ICMP Traffic
  ACL에서 허용
Interface | Routing | Gateway
Outside | Static | 43.43.5.2
Inside | Static | 43.43.2.250
DMZ3 | Static | 43.43.3.4

## Slide 5: Admin/R1 Context Detail
Interface | Nameif | Interface Type | Severity Level | IP address | Vlan
E1 | - | Physical | - | - | -
E1.22 | Inside | Logical | 100 | 43.43.2.253 | 22
E1.4 | Outside | Logical | 50 | 43.43.4.253 | 4
Interface | Nameif | Interface Type | Severity Level | IP address | Vlan
E1 | - | Physical | - | - | -
E1.22 | Inside | Logical | 100 | 43.43.2.253 | 22
E1.4 | Outside | Logical | 50 | 43.43.4.253 | 4

## Slide 6: ASA Redundant Interface
Interface | Member- interface | Nameif | Security Level | Context | IP address
Redundant 1 | E0 | outside | 0 | Admin | 43.43.5.253/24
 | E3 |  |  | R1 | 43.43.5.251/24
Interface | Routing | Gateway
Redundant1 | default | 43.43.5.2

## Slide 7: Active-Active Failover on ASA
Lan-based A-A Failover
  ASA1
    Admin: active
  ASA2
    R1: active
Failover Lan Interface
  E2 in vlan 100
  Active
    43.43.100.100/24
  Standby
    43.43.100.101/24

## Slide 8: Address Translation
Admin context
  Nat-control 설정
  Dynamic Address Translation
    SW4  R2 f0/0 Telnet
      43.43.5.100으로
    SW4  R2 f0/0 ICMP
      43.43.5.99로
  내부 DNS Server 질의
    내부 웹서버: 43.43.2.151
    외부 DNS Server: 43.43.5.151
R1 context
  R1 f0/0 Subnet
  R1 lo0
    ASA outside갈 때 Self-translated 되도록